## Slide 1: Advance LED and LASER Structures Including Quantum Well Structures By Karin Larson 4/25/16
Abstract: This presentation introduces the difference between LED and LASER diodes, their four main structures, and basic emissions.

## Slide 2: Outline
LED vs LASER
Homostructure
Single Heterostructure
Double Heterostructure
Quantum Wells
Edge and Surface Emissions

## Slide 3: LED and LASER
Electroluminescence
Reliable and long lifespan due to small size
Mass produced at low cost
Release a photon by an electron moving from a high state to a lower one

## Slide 4: LED
Light Emitting Diode
Mostly Monochromatic
Light from spontaneous emission
Significantly divergent
Incoherent light

## Slide 5: LASER
Light Amplification by Stimulation of Emitted Radiation
Single wavelength
Light by stimulated emission
Little divergence
Coherent light

## Slide 6: Homostructure
p-n homojuction
Both p and n are heavily doped
Excess carriers are spread by diffusion
Thickness of the active region is generally a few micrometers
Impractical for LASER diodes

## Slide 7
(Liu)

## Slide 8: Single Heterostructure
Replace p region with a P-p heterojunction to restrict diffusion
Creates a P-p-n diode
Causes a defined active layer in p region

## Slide 9
(Liu)

## Slide 10: Double Heterostructure
Can be either P-p-N or P-n-N
There is now a heterojunction on each side of the active region
Better than single heterostructures
Active region 100-300nm
High efficiency and large optical gain
Less absorption loss

## Slide 11
(Liu)
(Treharne)

## Slide 12
("Crédits Des Ressources.")

## Slide 13: Quantum Well
Double heterostructure when the active region is much smaller
Splits conduction and valence bands into sub-bands
The required injection current density is required than of a DH
Much higher gain
Gain bandwidth is typically 20-40THz

## Slide 14
(Liu)

## Slide 15
(Liu)

## Slide 16: Edge Emission
Categorized by broad-area and stripe-geometry
(Liu)

## Slide 17: Surface Emission
Categorized into broad and small area
(Liu)

## Slide 18: Conclusion
In general LEDs and LASER diodes have a lot of similarities with a few defining differences
Adding in heterojunctions leads to more control over the active region and refining the refractive index
Quantum wells are DH structures with a reduced active region and are much better
Light emissions can either be from the edge or the surface of the diode

## Slide 19: References
"Crédits Des Ressources." Specific Applications of Sensors for Photonic and Imaging. N.p., n.d. Web. 20 Apr. 2016. <http://www.optique-ingenieur.org/en/courses/OPI_ang_M05_C04/co/OPI_ang_M05_C04_web_2.html>.
Farrell, Gerald. "Laser Structures." Optical Communications Systems: Semiconductor Laser Diodes (n.d.): n. pag. Laser Structures. Dublin Institute of Technology, 2002. Web. 20 Apr. 2016. <http://www.electronics.dit.ie/staff/gfarrell/LaserPhotodiodes/4Laserdiodestruct.pdf>.
Larsen, Adrien P. "LASER vs. LED: What’s the Difference?" Acupuncture Technology News. N.p., 11 Feb. 2014. Web. 20 Apr. 2016. <https://www.miridiatech.com/news/2014/02/laser-vs-led-whats-the-difference/>.
Liu, Jia-Ming. "Semiconductor Lasers and Light Emitting Diodes." Photonic Devices. Cambridge: Cambridge, 2005. N. pag. Knovel. Web. 20 Apr. 2016.
"Potential Well." Wikipedia. Wikimedia Foundation, n.d. Web. 20 Apr. 2016. <https://en.wikipedia.org/wiki/Potential_well>.
Treharne, Robert. "Lecture 5: Junctions." Lecture 5: Junctions. Slide Share, 6 Nov. 2014. Web. 20 Apr. 2016. <http://www.slideshare.net/RobertTreharne/lecture-5-junctions>.
"Quantum Well Laser." Wikipedia. Wikimedia Foundation, n.d. Web. 20 Apr. 2016. <https://en.wikipedia.org/wiki/Quantum_well_laser>.

## Slide 20: 5 Key Points
The main differences between LED and LASER diodes are emission, divergence and coherence
The 4 structures are homostructure, single and double heterostructures, and quantum wells
Quantum wells are DH’s with a smaller active region
Light emissions are either from the edge of the diode or the surface
In general LEDS have a broader emission configuration while LASER uses smaller